## Slide 1: Experience with Using Remote Monitoring in Dam Emergency Response
National Dam Safety Program Technical Seminar | February 23 - 24, 2022

## Slide 2: Presentation Outline
Background
Dam Emergency Response
Remote Monitoring System
Remote Monitoring Data Management
Remote Monitoring Station Maintenance
Summary and Good Practices

## Slide 3: Background
Notes: Divider Slide

## Slide 4: Montgomery County, MD
Area: 507 sq mile
Population: 1.1 million
19 Municipalities

## Slide 5: Dam Hazard Classification
MDE Dam Safety Program
Dam Owner’s Responsibilities:
  Inspections
  Operation and Maintenance
  Emergency Action Plans (EAPs)

## Slide 6: Dams in Montgomery County
Majority Earthen Dams
16 High Hazard Dams
15 Significant Hazard Dams

## Slide 7: DEP’s Responsibilities
DEP is currently responsible for
8 Dams and 2 Levees
  Crabbs Branch Dam
  Gudelsky Pond Dam
  Railroad Branch Dam
  Wheaton Branch Dam
  Chadswood Dam
  Gunners Lake Dam
  Manchester Farm Pond Dam
  Montgomery Airpark Dam
  Montclair Manor Levee
  Turkey Branch Levees

## Slide 8: July 28th & 29th, 2017 Severe Rainfall Event
WHEATON BRANCH

## Slide 9: July 28th & 29th, 2017 Severe Rainfall Event (2)
WHEATON BRANCH on 7/28
UPSTEAM OF DENNIS AVE. BOX CULVERT

## Slide 10: Dam Emergency Response

## Slide 11: Dam Emergency Response (2)
DEP’s Emergency Response governed by Emergency Action Plans (EAPs)
Share responsibility with other County’s departments (OEMHS, Police, Fire, DOT, and others)
  DEP Staff in Emergency Operation Center (EOC)
DEP Dam Monitoring Procedures

## Slide 12: When Do We Mobilize?
Start monitoring remotely: precipitation and water levels
Activation: Full Mobilization – when rainfall amounts as predicted by NWS are:
  3” rain in 6 hours
  4” rain in 12 hours
  5” rain in 24 hours
Use of remote monitoring during the dam safety emergency event

## Slide 13: Wheaton Branch During Hurricane Ida
Date/Time(EST5EDT) | Precipitation(in)
Total 6 hr Precipitation | 2.02
Total 12 hr Precipitation | 2.11
Total 24 hr Precipitation | 2.69

## Slide 14: Wheaton Branch During Hurricane Ida (2)

## Slide 15: Benefits of Using Remote Monitoring System
Monitor water levels in real time for detection of rising water levels and provide early warnings about high water levels or flooding.
Alert County staff, first responders, property owners, communities, and residents to potential flood hazards
Get the right data in-time to make critical decisions.
Help preserve infrastructure, protect lives and properties
Access data from anywhere
Easily share important data through graphs, notifications, alarms and data reports

## Slide 16: Remote Monitoring System
Notes: Divider Slide

## Slide 17: History on Remote Monitoring
2006 County acquired remote monitoring system under a contract with Sutron
5 stations installed
In 2018 one additional station with camera was installed
Originally used radio signal. Switched to Cellular signal
Originally used Pressure Transducers. Later switched to Bubblers
4 new stations to be installed in 2022

## Slide 18: Existing Remote Monitoring Stations
Dams with Monitoring Stations
  Wheaton Branch Dam
  Crabbs Branch Dam
  Gudelsky Pond Dam
  Railroad Branch Dam
  Gunners Lake Dam
Dennis Ave Bridge Station
Stage 3
Stage 2
Staff Gauge
Hydromet Monitoring Station
Riser Structure

## Slide 19: Remote Monitoring System Components
Data Management
System Integration
Equipments

## Slide 20: Equipment
Tower
Power Supply (Solar, Battery)
Tipping Bucket Rain Gauges
Modem
Sutron Xlite 9210 Data Logger
Water Level Sensor (Pressure Transducer, Bubbler)
Rain Gauge
Enclosure Boxes
Solar Panel
Bubbler

## Slide 21: Example of Station Construction – Civil Work
Trench Excavation
Forming Tower Base
Conduit for the orifice

## Slide 22: Water Level Gauge – Sutron Bubbler
Advantages
No expensive equipment in the water
No damage during flood conditions
Self cleaning
Important to know
Best practices to install bubbler line

## Slide 23: Remote Monitoring System Integration
System Integration Based on County Needs
  Water Level Sensor (Bubbler or Pressure Transducer)
  Remote Real-time Data Acquisition (Data Logger)
  Communications (Mobile Data Transmission)
  Data Management Software (HydrometCloud)
Factory Assembly and Testing
Deliver and Install Station

## Slide 24: Remote Monitoring Data Management
Notes: Divider Slide

## Slide 25: Hydromet Cloud
Cloud-based Data Hosting Site
View-Analyze-Download Station Data
  http://hydrometcloud.com
24/7 Real Time Access of Station Data
Interactive Google Maps with Station Tabs for Current Data
Map Marker Color Coded for Alarms (Yellow, Red)
Live Images
Data Reports

## Slide 26: Data Report
Display Data for Select Parameters
Define Time Range
Export to Tables, Excel
Plot to Graphs

## Slide 27: Graph - Battery

## Slide 28: Graph - Precipitation

## Slide 29: Graph – Water Level

## Slide 30: Hydromet Cloud Mobile App
Mobile Phone
Tablet

## Slide 31: Hydromet Cloud Mobile App (2)
Graphs
Custom Plots

## Slide 32: Alarms and Notifications
Alarms Set Up through Hydromet Cloud
Alarms on Battery, Precipitation, and Water Levels

## Slide 33: Remote Monitoring Station Maintenance

## Slide 34: Station Maintenance
Implement Station Maintenance Bi-annually
  Inspect Equipment Conditions, Connections and Power Supply Components
  Check Power Supply Status
  Disassemble and Clean Tipping Bucket Rain Gauges
  Calibrate Stage Logger to Staff Gauge Readings
  Replace Desiccants
  Clean Camera Lens

## Slide 35: Station Maintenance (2)
Monitor Station Weekly through HydrometCloud
Address Station Repair Needs
  Battery Replacement
  Solar Panel Vandalism
  Sensor Replacement
  Bubbler Cable Repair
  Rain Gauge Repair
Upgrade Station Equipment as Needed
Download Historical Data Twice A Year

## Slide 36: Summary and Good Practices
Remote Monitoring System – A Great Tool to Use During Dam Emergency Response
Access Extensive Data through Hydromet Cloud
Provide Early Warning on Flooding
Get the Right Data in-time to Make Critical Decisions
Implement Station Maintenance Bi-annually
Monitor Station Status Weekly through Hydromet Cloud
Address Station Repair and Upgrade Needs
Download Data to Track Long Term Station Performance

## Slide 37: Questions?
Leying Zhang
Montgomery County DEP
Email: Leying.Zhang@montgomerycountymd.gov
Gene Gopenko
Montgomery County DEP
Email: Gene.Gopenko@montgomerycountymd.gov